## Slide 1
EPS Colloquium, Harvard
Cambridge, MA
May 5, 2014
83520601
Arlene M. Fiore
Acknowledgments: Olivia Clifton, Gus Correa, Nora Mascioli, Lee Murray, Luke Valin (CU/LDEO), Harald Rieder (U Graz, Austria), Elizabeth Barnes (CSU), Alex Turner (Harvard)
Larry Horowitz (GFDL), Vaishali Naik (UCAR/GFDL), Meiyun Lin (Princeton/GFDL)
U.S. air pollution and climate:
Trends, variability, and interactions
Haze over Boston, MA
http://www.airnow.gov/index.cfm?action=particle_health.page1#3

## Slide 2
Ozone and Particulate Matter (PM)
are the top two U.S. air pollutants
Millions of people living in counties with air quality concentrations above the level of the U.S. National Ambient Air Quality Standards
One or more NAAQS
Ozone (8-hour)
PM2.5 (annual/24-hr)
PM10 (24-hr)
SO2 (1-hr)
PM10 (24hr)
Lead (3-month)
NO2 (annual/1-hr)
CO (8-hr)
0 20 40 60 80 100 120 140 160
2012
142.2
133.2
28.2
16.1
15.1
8.1
EPA, 2014: http://www.epa.gov/airtrends/aqtrends.html#comparison

## Slide 3: Air pollutants and their precursors contribute to climate forcing from preindustrial to present
IPCC AR5 WG1 SPM (2013)
Regulated in U.S.
as precursors
to ground-level O3
Anthropogenic greenhouse gases methane + tropospheric ozone together contribute ~1/2 (abundance) to 2/3 (emissions) of CO2 radiative forcing
(Lifetimes must also be considered: CO2 dominates long-term)
Net cooling from aerosols opposes
GHG warming
Warming 
 Cooling

## Slide 4
Ground-level O3 is photochemically produced from regional sources (natural + anthrop.) that build on background levels
O3
+
CH4
CO
NMVOC
NOx
Fuel local-to-regional ozone
pollution episodes
Raise background ozone levels

## Slide 5: The U.S. ozone smog problem is spatially widespread
Exceeds
standard
(24% of sites)
http://www.epa.gov/airtrends/2011/index.html
4th highest maximum daily 8-hr average (MDA8) O3 in 2010
High-O3 events typically occur in
-- densely populated areas (sources)
-- summer (favorable meteorology)
FUTURE?
 Lower threshold (60-70 ppb [Federal Register, 2010]) would greatly expand non-attainment regions
Estimated benefits from a ~1 ppb decrease in surface O3:
~ $1.4 billion (agriculture, forestry, non-mortality health) within U.S. [West and Fiore, 2005]
~ 500-1000 avoided annual premature mortalities within N. America [Anenberg et al., 2009]

## Slide 6: Trends in summer daytime (11am-4pm) average ozone at rural U.S. monitoring sites (CASTNet): 1990 to 2010
Cooper et al., JGR, 2012
Success in decreasing highest levels, but baseline rising (W. USA)
Decreases in EUS attributed in observations and models to NOx emission
controls in late 1990s, early 2000s [e.g., Frost et al., 2006; Hudman et al., 2007; van der A. et al., 2008; Stavrakou et al., 2008; Bloomer et al., 2009, 2010; Fang et al., 2010]
significant
not significant
95%
5%
ppb yr-1

## Slide 7: The “tightening vise” of ozone management
Ozone concentration
Historical
Future
(alternate view)
Hemispheric
background
Regional
Local
Standard
Future
Keating, T. J., J. J. West, and A. Farrell (2004) Prospects for international management of intercontinental air pollutant transport, in A. Stohl, Ed., Intercontinental Transport of Air Pollution, Springer, p. 295-320.
 Future may require concerted efforts to lower background

## Slide 8: Surface temperature and O3 are correlated on daily to inter-annual time scales in polluted regions [e.g., Bloomer et al., 2009; Camalier et al., 2007; Cardelino and Chameides, 1990; Clark and Karl, 1982; Korsog and Wolff, 1991]
Implies that changes in climate will influence air quality
Observations at U.S. EPA CASTNet site Penn State, PA 41N, 78W, 378m
July mean MDA8 O3 (ppb)
10am-5pm avg
pollutant sources
Degree of mixing
1. Meteorology (e.g., air stagnation)
What drives the observed O3-Temperature correlation?
T
NOx
T-sensitive
NOx reservoir
NMVOCs
Deposition
2. Feedbacks (Emis, Chem, Dep)

## Slide 9
Models estimate a ‘climate change penalty’ (+2 to 8 ppb) on surface O3 over U.S. but often disagree in sign regionally
Uncertain regional climate responses (and feedbacks) to global warming
Model estimates typically based on a few years of present and future (often 2050s) meteorology from 1 realization of 1 GCM
Modeled changes in summer mean of daily max 8-hour O3 (ppb; future – present)
NE MW WC GC SE
Weaver et al., BAMS, 2009
ppbv
Wu et al., JGR, 2008:
“Climate Penalty”

## Slide 10: ‘First-look’ future projections with current chemistry-climate models for N. Amer. Surface O3 (emissions + climate change)
V. Naik, adapted from Fiore et al., 2012; Kirtman et al., 2013 (IPCC WG1 Ch 11)
RCP8.5
RCP6.0
RCP4.5
RCP2.6
Decadal time slice simulations
(2-12 models)
A major advance to have coupled atmospheric chemistry in climate models
Trends mainly reflect ozone precursor emission pathways
Annual, continental-scale means reveal little about drivers of regional change
Multi-
model
Mean
Range across
ACCMIP CCMs
Multi-model Mean
Range across
CMIP5 CCMs
North America
Annual mean spatially averaged (land only) O3 in surface air
Transient simulations
(4 models)

## Slide 11: How and why might extremes change?
Mean
shifts
Variability
increases
Symmetry
changes
Figure SPM.3, IPCC SREX 2012
http://ipcc-wg2.gov/SREX/
How do different processes influence the overall distribution?
Meteorology (e.g., stagnation vs. ventilation)
 Shift in mean?
 Change in symmetry?
Changing global emissions (baseline)
Changing regional emissions (episodes)
Feedbacks (Emis, Chem, Dep)
Does climate forcing from air pollutants influence regional climate extremes?
Aerosols vs. greenhouse gases
How do changes in the balance of these processes alter the seasonal cycle?
NE US: regional photochemistry (summer)
vs. transported background

## Slide 12: Approach: Targeted sensitivity simulations in a chemistry-climate model to examine chemistry-climate interactions
Tool: GFDL CM3 chemistry-climate model
~2°x2° horizontal resn.; 48 vertical levels
Over 6000 years of climate simulations that include chemistry (air quality)
Options for nudging to re-analysis + global high-res ~50km2 [Lin et al., 2012ab; 2014]
Donner et al., J. Climate, 2011;
Golaz et al., J. Climate, 2011;
John et al., ACP, 2012
Turner et al., ACP, 2012
Levy et al., JGR, 2013
Naik et al., JGR, 2013
Barnes & Fiore, GRL, 2013
O3
+
CH4
CO
NMVOC
NOx
Emission (CH4 abundance) pathways prescribed
Biogenic emissions held constant
Lightning NOx source tied to model meteorology
O3, (aerosols, etc.), affect simulated climate

## Slide 13: Approach: Historical + Future global change scenarios & targeted sensitivity simulations in GFDL CM3 CCM
Scenarios developed by CMIP5 [Taylor et al., BAMS, 2012] in support of IPCC AR5 [e.g., Cubasch et al., 2013; Ch 1 WG 1 IPCC (see Box 1.1)]
Preindustrial control (perpetual 1860 conditions >800 years)
(2) Historical (1860-2005) [Lamarque et al., 2010]
  All forcings (5 ensemble members)
  Greenhouse gas only (3)
  Aerosol only (3)
(3) Future (2006-2100): Representative Concentration Pathways
(+ perturbations)
 evaluate with observations
RCP8.5 (3)
RCP4.5 (3)
Percentage change: 2005 to 2100
Global
CO2
Global
CH4
Global
NOx
NE USA
NOx
 CMIP5/AR5 [van Vuuren, 2011; Lamarque et al., 2011; Meinshausen et al., 2011]
 Isolate role of warming climate
 Quantify role of rising CH4 (vs. RCP8.5)
RCP8.5_WMGG (3)
RCP4.5_WMGG (3)
RCP8.5_2005CH4

## Slide 14: In polluted (high-NOx) regions, surface O3 typically peaks during summer (monthly averages at 3 NE USA measurement sites)
Feb Apr Jun Aug Oct Dec
Monthly 1991-1996 averages across 3 NE USA sites
Clean Air Status and Trends Network (CASTNET)
Regionally
Representative sites
[Reidmiller et al., ACP, 2009]
O. Clifton
Notes: Danger level

## Slide 15: Shifting surface ozone seasonal cycle evident in observations over NE USA
Feb Apr Jun Aug Oct Dec
Monthly averages across 3 NE USA sites
Clean Air Status and Trends Network (CASTNET)
Regionally
Representative sites
[Reidmiller et al., ACP, 2009]
O. Clifton
Summer ozone decreases; shift towards broad spring-summer maximum
following EUS NOx controls (“NOx SIP Call”)
1991-1996
2004-2009
Notes: Danger level

## Slide 16: Structure of observed changes in monthly mean ozone captured by GFDL CM3 CCM (despite mean state bias)
Feb Apr Jun Aug Oct Dec
Monthly averages across 3 NE USA sites
Regionally
Representative sites
[Reidmiller et al., ACP, 2009]
O. Clifton et al., submitted
OBS (CASTNet)
CM3 (Model)
1991-1996
2004-2009
CM3 NE US shows summer O3 decrease, small winter increase from ~25% decrease in NOx emissions
(applied year-round)
[see also EPA, 2014; Parrish et al., GRL, 2013 find shifts at remote sites]
Notes: Danger level

## Slide 17: Reversal of surface O3 seasonal cycle occurs in model under scenarios with dramatic regional NOx reductions
2005 to 2100 % change
CH4
Global
NOx
NE USA
NOx
NE USA evolves from “polluted” to “background” over the 21st C
Reversal occurs after 2020s (not shown)
Clifton et al., submitted
2006-2015
2006-2015
2091-2100
2091-2100
RCP4.5
RCP8.5
Feb Apr Jun Aug Oct Dec
?
Decreasing NOx emissions  lower summer O3
3 ensemble members for each scenario
Notes: Non polluted region

## Slide 18: Doubling of global CH4 abundance (RCP8.5) raises NE USA surface ozone in model; largest impact during winter
Feb Apr Jun Aug Oct Dec
Doubling of methane increases surface O3 background by 6-11 ppb
2006-2015
2006-2015
2091-2100
2091-2100
RCP8.5_2005CH4
RCP8.5
Clifton et al., submitted

## Slide 19: “Climate penalty” on monthly mean NE USA surface O3 as simulated with the GFDL CM3 model
Feb Apr Jun Aug Oct Dec
JJA NE USA Temp (sfc) +2.5ºC
Feb Apr Jun Aug Oct Dec
2006-2015
2006-2015
2091-2100
2091-2100
RCP8.5_WMGG
RCP4.5_WMGG
JJA NE USA Temp (sfc) +5.5ºC
“Penalty” limited to increases during warmest months
Extends into May and September in high warming scenario
Fully offset by regional precursor emission reductions under RCPs
Clifton et al., submitted
Notes: And so we also see a broadening ..
So we conclude …

## Slide 20: How and why might air pollution extremes change?
Mean
shifts
Variability
increases
Symmetry
changes
Figure SPM.3, IPCC SREX 2012
http://ipcc-wg2.gov/SREX/
How do different processes influence the overall distribution?
Meteorology (e.g., stagnation vs. ventilation)
 Shift in mean?
 Change in symmetry?
Changing global emissions (baseline)
Changing regional emissions (episodes)
Feedbacks (Emis, Chem, Dep)
Does climate forcing from air pollutants influence regional climate extremes?
Aerosols vs. greenhouse gases
How do changes in the balance of these processes alter the seasonal cycle?
NE US: regional photochemistry (summer)
vs. transported background
[
not today]
Notes: Add something here on role of aerosol vs. greenhouse gas forcing.

## Slide 21: Under RCPs, NE USA high-O3 summertime events decrease; beware ‘penalty’ from rising methane (via background O3)









2006-2015
2016-2025
2026-2035
2036-2045
2046-2055
2056-2065
2066-2075
2076-2085
2086-2095
RCP4.5:
Moderate
warming
Time
RCP8.5:
Extreme
warming
Time
RCP8.5
RCP4.5
2005 to 2100 % change
CH4
Global
NOx
NE USA
NOx
 Rising CH4 in RCP8.5 partially offsets O3 decreases otherwise attained with regional NOx controls (RCP4.5)
H. Rieder
June-July-August GFDL CM3 MDA8 O3 (ppb)

## Slide 22: GFDL CM3 generally captures NE US JJA surface O3 decrease following NOx emission controls (-25% early 1990s to mid-2000s)
Rieder et al., in prep
Implies bias correction based on present-day observations can be applied to scenarios with NOx changes (RCPs for 21st C)
Focus on upper half of distribution
Observed
(CASTNet)
GFDL CM3 Model
JJA MDA8 O3 (ppb)
Relative Frequency

## Slide 23: Characterizing observed ‘extreme’ ozone pollution events
JJA MDA8 O3 1987-2009 at CASTNet Penn State site
Gaussian (ppb)
Observed MDA8 O3 (ppb)
Observed MDA8 O3 (ppb)
Generalized Pareto Distribution Model (ppb)
EVT Approach:
(Peak-over-threshold)
for MDA8 O3>75 ppb
Gaussian:
Poor fit
for extremes
1988-1998
1999-2009
Rieder et al., ERL 2013
 Extreme Value Theory (EVT) methods describe the high tail of the observed ozone distribution (not true for Gaussian)

## Slide 24: EVT methods enable derivation of probabilistic “return levels” for JJA MDA8 O3 within a given “return period”
CASTNet site: Penn State, PA
Rieder et al., ERL 2013
1988-1998
1999-2009
Sharp decline in return levels
from 1988-1998 to 1999-2009; longer return periods for a given event
(attributed to NOx emission controls)
Consistent with prior work [e.g., Frost et al., 2006; Bloomer et al., 2009, 2010]
New approach to translates air pollution changes into probabilistic language
Apply methods to 23 EUS CASTNet sites to derive
1-year return levels
 Decreased by 2-16 ppb
 Remain above 75 ppb
Notes: Prep GPD // Rieder 2013

## Slide 25: Large NOx reductions offset climate penalty on O3 extremes
1-year Return Levels in CM3 chemistry-climate model (corrected)
Summer (JJA) MDA8 Surface O3
ppb
2046-2055
RCP4.5_WMGG:
Pollutant emissions held constant (2005) +
climate warming
2091-2100
RCP4.5:
Large NOx decreases +
climate warming
All at or below 60 ppb
Nearly all at or below 70 ppb
Rieder et al., in prep
 We find a simple relationship between NOx reductions and 1-year return levels

## Slide 26: A mechanism underlying ‘climate penalty’: Frequency of NE US summer storms decreases as the planet warms…
RCP4.5
RCP8.5 (1 ens. member)
Turner et al., ACP, 2013
Region for counting storms
Region for counting O3 events
Number of storms per summer in the GFDL CM3 model,
as determined from applying
the MCMS storm tracker [Bauer et al., 2013]
to 6-hourly sea level pressure fields
(follows approach of Leibensperger et al., 2008)
(3 ens.
members)
Trends are significant relative to variability in preindustrial control simulation

## Slide 27: …but the storm count – O3 event relationship is weaker than derived from observations
Detrended O3 pollution days
Detrended Number of mid-latitude cyclones
Observed relationship
[Leibensperger et al, ACP, 2008]
Slope = -4.2 O3 events/storm
1980-2006:
NCEP/NCAR Reanalysis 1 & AQS ozone
Simulated relationship (GFDL CM3)
[Turner et al., ACP, 2013]
 Model problem (bias/process representation)?
Change in drivers (under warming climate)?
Decadal variability in strength of relationship?
RCP4.5_WMGG 2006-2100
Can we find a simpler diagnostic of large-scale circulation changes?
Slope = -2.9 O3 events/storm

## Slide 28
Peak latitude of summertime surface O3 variability over Eastern N. America follows the jet (500 hPa) as climate warms
Barnes & Fiore, GRL, 2013
Each point = 10 year mean (over ensemble members)
RCP4.5_WMGG
 Decadal variability
Relevance to shorter periods?
Differences in model jet position lead to inter-model differences in AQ response?
O3-Temperature
relationship (not shown)
also aligns with jet latitude
 Historically observed relationships may not hold if large-scale circulation shifts
Latitude of max std. dev. of JJA MDA8 O3 (deg N)
RCP8.5: most warming,
Largest jet shift
RCP8.5
jet: 2086-2095
jet: 2006-2015
change in O3 std. dev. (ppb)

## Slide 29: How and why might air pollution extremes change?
Mean
shifts
Variability
increases
Symmetry
changes
Figure SPM.3, IPCC SREX 2012
http://ipcc-wg2.gov/SREX/
How do different processes influence the overall distribution?
Meteorology (e.g., stagnation vs. ventilation)
 Shift in mean?
 Change in symmetry?
Changing global emissions (baseline)
Changing regional emissions (episodes)
Feedbacks (Emis, Chem, Dep)
Does climate forcing from air pollutants influence regional climate extremes?
Aerosols vs. greenhouse gases
How do changes in the balance of these processes alter the seasonal cycle?
NE US: regional photochemistry (summer)
vs. transported background
[
not today]
Notes: Add something here on role of aerosol vs. greenhouse gas forcing.

## Slide 30: Offsetting impacts on extreme temperature events from greenhouse gases vs. aerosol over historical period
N. Mascioli
-4.0 -2.0 0.0 2.0 4.0
Change in Hottest Days (°C)
Greenhouse Gas Only
Aerosol Only
Consistent (?) patterns (spatial correlation r = 0.56 )
Pollutants  regional weather events  extreme pollution?
Single forcing historical simulations in GFDL CM3
(all other forcings held at 1860 conditions)
(1976-2005) – (1860-1889)
(annual maximum daily temperature [e.g., Sillman et al., 2013ab])
X = outside range of variability (95%) of differences between 30-year intervals in preind. control simulation

## Slide 31: Increase in hottest days projected throughout 21st Century under extreme warming scenario
N. Mascioli
 Amplified warming during extreme events from aerosol removal?
 Preferred response patterns?
-4.0 -2.0 0.0 2.0 4.0
Change in Hottest Days (°C)
-8.0 -4.0 0.0 4.0 8.0
Change in Hottest Days (°C)
(annual maximum daily temperature [e.g., Sillman et al., 2013ab])
GFDL CM3 1 ensemble member, RCP8.5 scenario: aerosols decline, GHGs rise
mid-21stC: (2035-2065) – (2006-2036)
late-21stC: (2070-2100) – (2006-2036)
X = outside range of variability (95%) of differences between 30-year intervals in preind. control simulation
Notes: Mention also looking precip

## Slide 32: Atmospheric Chemistry Group at LDEO/CU
On the roof of our building following mid-Dec snowfall
(missing from photo: undergraduate researcher Jean Guo)
Harald
Nora
Gus
Arlene
Luke
Olivia
Lee

## Slide 33
U.S. air pollution and climate: Trends, variability, and interactions
Relevant to model differences in O3 response to climate?
[Weaver et al., 2009; Jacob & Winner, 2009; Fiore et al., 2012]
Zonal O3 variability aligns with the 500 hPa jet over NE NA (JJA)
Decadal jet shifts can influence O3:T [Barnes & Fiore, 2013]
NOx reductions reverse the O3 seasonal cycle over NE USA
Will NE US evolve to ‘background’ air quality over the 21st C?
Detecting chemistry-climate interactions
Will (global) aerosol removal amplify response of U.S. climate extremes to rising GHGs?
New approach to characterize pollution events [Rieder et al., 2013]
Double ‘penalty’ on NE US O3 from climate change + rising CH4?
RCP4.5
Time
RCP8.5
Rising CH4 + decreasing NOx shift balance of regionally produced vs. transported O3
Time
Translation to probabilistic language,”1-year event”, useful for decadal planning?