## Slide 1
SIPA ESP MPA Program
LDEO, Palisades, NY
July 1, 2013
83520601
Arlene M. Fiore
www.ldeo.columbia.edu/~amfiore
Ozone smog in surface air:
“Background” contributions and climate connections
Haze over Boston, MA
http://www.airnow.gov/index.cfm?action=particle_health.page1#3

## Slide 2: The U.S. ozone smog problem is spatially widespread, affecting ~108 million people [U.S. EPA, 2012]
Exceeds
standard
(24% of sites)
http://www.epa.gov/airtrends/2011/index.html
4th highest maximum daily 8-hr average (MDA8) O3 in 2010
High-O3 events typically occur in
-- densely populated areas (local sources)
-- summer (favorable meteorological conditions)
Future?
 Lower threshold would greatly expand non-attainment regions

## Slide 3
Tropospheric O3 formation & “Background” contributions
Continent
NMVOCs
CO
NOx
+
O3
Fires
Biosphere
Human
activity
Ocean
METHANE (CH4)
stratosphere
lightning
“Background” ozone
Natural
sources
Continent
X
X
intercontinental transport
Notes: Emphasie WUS // EUS…

## Slide 4: Setting achievable standards requires accurate knowledge of background levels
120 ppb
1979
1-hr avg
84 ppb
1997
8-hr
75 ppb
2008
8-hr
40
60
80
100
120
O3 (ppbv)
20
U.S. National Ambient Air Quality Standard
for O3 has evolved over time
Future?
(proposed)
typical U.S.
“background”
(model estimates)
[Fiore et al., 2003;
Wang et al., 2009;
Zhang et al., 2011]
Allowable O3 produced from U.S. anthrop. sources (“cushion”)
Lowering thresholds for U.S. O3 NAAQS implies thinning cushion between regionally produced O3 and background
background
events over WUS
[Lin et al., 2012ab]
Clean Air Act has provisions for States to be exempted from pollution beyond their control but in practice may need clarification

## Slide 5
Some challenges for WUS O3 air quality management
Asia
Pacific
stratosphere
lightning
Wildfire, biogenic
Western USA
Rising Asian emissions
[e.g., Jacob et al., 1999;
Richter et al., 2005;
Cooper et al., 2010]
Natural events e.g., stratospheric [Langford et al [2009]; fires [Jaffe & Wigder, 2012]
Warming climate
+in polluted regions
[Jacob & Winner, 2009 review]
+ natural sources
[recent reviews: Isaksen et al., 2009; Fiore et al., 2012]
? Transport pathways
Need process-level understanding on daily to multi-decadal time scales
X
methane
“Background Ozone”
intercontinental
transport
Notes: Emphasie WUS // EUS…

## Slide 6
Estimates of Asian and stratospheric influence on
WUS surface ozone in spring
TOOL: GFDL AM3 chemistry-climate model [Donner et al., J. Clim. 2011]
~50x50 km2 Jan-Jun 2010 – overlaps period of intensive field measurements (CalNex)
Nudged to GFS (“real”) winds – allows direct comparison with snapshot observations
Fully coupled chemistry in the stratosphere and troposphere within a climate model
Do they influence high-O3 events in populated regions?
Mean MDA8 O3 in surface air
Asian: May-June 2010
0
2
6
4
8
O3 (ppb)
Base Simulation – Zero Asian
anth. emissions
[Lin et al., JGR, 2012a]
O3 (ppb)
Stratospheric (O3S): April-June 2010
Tagged above e90 tropopause [Prather et al., 2011] + subjected to same loss processes as tropospheric O3.
[Lin et al., JGR, 2012b]
Notes: 6

## Slide 7: Stratosphere-to-troposphere (STT) O3 transport influence on WUS high-O3 events
Ongoing work exploring development of space-based indicators
AIRS, May 25-29
Altitude (km a.s.l.)
North  South
Sonde O3, May 28
300 hPa PV
Total column O3 [DU]
[ppb]
30
60
90
150
120
Would STT confound attainment of tighter
standards in WUS?
Are exceptional events accurately identified?
Surface MDA8 O3, May 29
TH
RY
PS
SN
JT
SH
15 25 35 45 55
[ppb]
M. Lin et al., JGR, 2012b
Model (AM3): stratospheric O3
Observed Total O3
Notes: mention that surface plots are published

## Slide 8: Asian O3 pollution over S. CA: Trans-pacific transport + subsidence to lower troposphere
 We find these events sometimes contribute to ‘pushing’ O3 in surface air above thresholds of 60 and 70 ppb [Lin et al., JGR, 2012a]
Satellite CO columns (AIRS)
May 8
May 6
May 4
[1018 molecules cm-2]
θ
[K]
Altitude (km a.s.l.)
Latitude (N S) along CA
[ppb]
10
20
0
30
GFDL AM3 Model Asian O3
Consistent with sonde and aircraft
[Lin et al., JGR, 2012a]

## Slide 9
GFDL AM3 (~2°x2°)
GEOS-Chem (½°x⅔°)
Average Springtime (March-April-May) North American background
MDA8 O3 in model surface layer
GFDL AM3: Generally more mixing of background O3 to the surface?
J. Oberman
ppb
Models differ in estimates of North American background
(estimated by simulations with N. American anth. emissions set to zero)
Model differences provide an error estimate
Need careful, process-oriented evaluation with observations
Notes: 9

## Slide 10: Air pollution-climate connection via methane
Possible at cost-savings / low-cost [West & Fiore 2005; West et al.,2012]
$1.4 billion (agriculture, forestry, non-mortality health) within U.S. alone [West and Fiore, 2005]
7700-400,000 annual avoided cardiopulmonary
premature mortalities in the N. Hemisphere
uncertainty in concentration-response relationship only [Anenberg et al., ES&T, 2009]
Range over
18 models
Global mean
avoided warming in 2050 (°C)
[WMO/UNEP, 2011]
CLIMATE
OZONE AIR QUALITY
N. America Europe East Asia South Asia
[Fiore et al., JGR, 2009; TF HTAP, 2007, 2010; Wild et al., ACP, 2012]
Benefits of ~25% decrease in global anthrop. methane emissions
Notes: Monetized co-benefits of methane mitigation for
human health are estimated to be $13–17 per ton CO2eq

## Slide 11
Models estimate ‘climate change penalty’ on surface O3 over wide U.S. regions but often disagree in sign regionally
Uncertain regional climate responses to global warming
Gap in analysis over much of mountainous West
How will background change? (e.g., frequency of fires, strat. intrusions)
Modeled changes in summer mean of daily max 8-hour O3 (ppb; future – present)
NE MW WC GC SE
Weaver et al., BAMS, 2009
Increases (2 to 8 ppb) in all models over large U.S. regions

## Slide 12
Ozone smog in surface air: background and climate connections-
Summary and intersections with public policy
http://science.house.gov/hearing/subcommittee-environment-background-check-achievability-new-ozone-standards
Background generally well below NAAQS thresholds in populated regions
High-altitude western U.S. is susceptible to natural events (stratospheric O3 intrusions; wildfires) and international pollutant transport
 formulation of standard (4th highest, 3 year average) allows some room
 ‘Exceptional event’ and ‘international transport’ provisions in Clean Air Act but implementation needs clarification
 Ongoing review (every 5 years) of science supporting O3 NAAQS; related Congressional hearing June 12, 2013
NASA Air Quality Applied Sciences Team (www.aqast.org):
Earth Science Serving Air Quality Management Needs
Climate warming expected to alter pollutant levels
 increase O3 in already polluted regions (‘climate penalty’)
 alter natural sources (wildfires, stratospheric, biogenic emissions)
 occur in context of future global and regional emission changes
Methane controls: ‘win-win’ for near-term climate, air quality; also economic
Climate and Clean Air Coalition (http://www.unep.org/ccac/)

## Slide 14: Strong correlations between surface temperature and O3 measurements on daily to inter-annual time scales in polluted regions [e.g., Bloomer et al., 2009; Camalier et al., 2007; Cardelino and Chameides, 1990; Clark and Karl, 1982; Korsog and Wolff, 1991]
Implies that changes in climate will influence air quality
Observations at U.S. EPA CASTNet site Penn State, PA 41N, 78W, 378m
July mean MDA8 O3 (ppb)
T
NOx
OH
PAN
H2O
VOCs
Deposition
2. Feedbacks (Emis, Chem, Dep)
10am-5pm avg
pollutant sources
Degree of mixing
1. Meteorology (e.g., air stagnation)
What drives the observed O3-Temperature correlation?

## Slide 15: Regional climate change over the NE USA leads to higher summertime surface O3 (“climate penalty” [Wu et al., JGR, 2008])
RCP4.5_WMGG 2091-2100
(2091-2100) – (2006-2015)
RCP4.5_WMGG 3 ens. member mean:
Moderate climate change increases NE USA surface O3 1-4 ppb in JJA
(agreement in sign for this region across prior modeling studies)
3 ensemble
members for each scenario
Monthly mean surface O3 over NE USA
RCP4.5_WMGG 2006-2015
GFDL CM3 chemistry-climate model
O. Clifton/H. Rieder
How does NE USA O3 respond to changing regional and global emissions?

## Slide 16: Extremes: The highest summertime surface O3 events over NE USA decrease strongly under NOx controls
RCP8.5
Time









2006-2015
2016-2025
2026-2035
2036-2045
2046-2055
2056-2065
2066-2075
2076-2085
2086-2095
RCP4.5
Time
RCP8.5
RCP4.5
2005 to 2100 % change
CH4
Global
NOx
NE USA
NOx
RCP8.5 vs. RCP4.5: Rising CH4 increases surface O3, at least partially offsetting gains otherwise attained via regional NOx controls
H. Rieder

## Slide 17
Asian pollution contributes to high-O3 events over S. CA
in the GFDL AM3 model (~50 km2 resolution)
25th percentile
~50% of MDA8 O3 > 70 ppbv would not have occurred without Asian O3
Lin et al., 2012a, JGR –AGU Editors’ Highlight, Science Shot, Nature News
Asian emissions contribute ≤ 20% of total O3 (local influence dominates)
Highest Asian enhancements for total ozone in the 70-90 ppbv range
Notes: Model bias does not have a direct relationship with Asian enhancements
for all land grids within the rectangle indicated in Figure 9a.
The blue line represents the 25th percentile value of Asian
enhancements. Points falling within the green and red trapezoids
denote values in excess of 60 and 70 ppbv, respectively,
that would not have occurred in the absence of
Asian emissions in the mode
17

## Slide 18
http://science.house.gov/hearing/subcommittee-environment-background-check-achievability-new-ozone-standards

## Slide 19: Clean Air Act includes provisions to allow states to be exempted from pollution influences beyond their control
Section 179B covers international pollutant transport:
“that the implementation plan…would be adequate to attain and maintain the [NAAQS]…but for emissions emanating outside the US.”
Section 319 (b)(3)(B) and 107(d)(3): Exceptional Events: “avoid…designating an area as nonattainment…if a state adequately demonstrates that an exceptional event has caused an exceedance or violation of a NAAQS. EPA is also requiring States to take reasoable meausres to mitigate the impacts of an exceptional event”
c/o Michael Ling, US EPA, from
WESTAR presentation October 2012
http://www.epa.gov/glo/SIPToolkit/documents/20070322_72fr_13560-13581_exceptional_events_data.pdf
 Requires accurate understanding of transported background events

## Slide 20: Satellite products indicate potential for contributions from transported “background”
9/15/12
Indicate potential downwind influence
Public health alerts
Identify exceptional events
Quantitative estimates require models
S.Dakota
Montana
Dugan Fire
9/15/12
NASA image courtesy Jeff Schmaltz, LANCE MODIS Rapid Response Team at NASA GSFC.
Fires: MODIS
http://earthobservatory.nasa.gov/
NaturalHazards/view.php?id=79221
Intercontinental transport: AIRS
Asian pollution forecasting with
AIRS CO columns (Lin et al., 2012a)
A. Fiore (CU/LDEO)
M. Lin (Princeton)
[DU]
[ppbv]
300 hPa PV
~550-350 hPa O3
Total Column O3
Stratospheric intrusions: OMI
Products from X. Liu, Harvard
correlation coefficient (r)
Notes: GRC; time lag 2 days

## Slide 21
Year
CH4 Abundance (ppb) past 1000 years
[Etheridge et al., 1998]
2000
1000
800
1200
1600
1400
1000
1500
Historical increase in atmospheric methane and ozone
(#2 and #3 greenhouse gases after carbon dioxide [IPCC, 2007])
Ozone at European mountain sites 1870-1990 [Marenco et al., 1994]
Preindustrial to present-day radiative forcing [Forster et al., (IPCC) 2007]:
+0.48 Wm-2 from CH4 +0.35 Wm-2 from O3

## Slide 22: How will surface O3 distributions evolve with future changes in emissions and climate?
Tool: GFDL CM3 chemistry-climate model
Donner et al., J. Climate, 2011;
Golaz et al., J. Climate, 2011;
John et al., ACP, 2012
Turner et al., ACP, 2012
Naik et al., submitted
Horowitz et al., in prep
~2°x2°; 48 levels
Over 6000 years of climate simulations that include chemistry (air quality)
Options for nudging to re-analysis + global high-res ~50km2 [Lin et al., JGR, 2012ab]
Climate / Emission Scenarios: Representative Concentration Pathways (RCPs)
RCP8.5
RCP4.5
RCP4.5_WMGG
Percentage changes from 2005 to 2100
Global
CO2
Global
CH4
Global
NOx
NE USA
NOx
Enables separation of roles of changing climate from changing air pollutants
Global T (°C) (>500 hPa)
Notes: Simplify – scenarios to test climate vs emissions impacts

## Slide 23: ‘First-look’ future projections with current chemistry-climate models for North American Ozone Air Quality
V. Naik, adapted from Fiore et al., 2012
RCP8.5
RCP6.0
RCP4.5
RCP2.6
Mean over
1986-2005 of
CMIP5 CCMs
Transient
simulations
(4 models)
1980+2000 mean of ACCMIP CCMs decadal time slice simulations
(2-12 models)
Annual mean spatially averaged (land only) O3 in surface air
Beyond annual, continental-scale means: Shifting balance of regional and baseline O3 changes seasonal cycles and daily distributions; Role of regional climate change?
Multi-
model
Mean
Range across
all models
Multi-model Mean
Range across
all models
Notes: Leave you with a pretty picture & overall conclusion in blue text

## Slide 24
satellites
suborbital platforms
models
AQAST
Pollution monitoring
Exposure assessment
AQ forecasting
Source attribution Quantifying emissions
Natural & foreign influences
AQ processes
Climate-AQ interactions
AQAST