Snapshot Day 10/12/06 Data

(Salt Front RM 52.5)

RIVER MILE 61E

Long Dock, Beacon

Latitude 42(15’.407” Longitude 73(48’.781”

Rebecca Johnson, NYS DEC Hudson River Estuary Program

Susan Hereth, Scenic Hudson

Linda Houlihan, Beacon 5th grade

Location: Long Dock in Beacon, Dutchess County NY

Area: Site is forested, open and grassy, includes a parking lot, used for picnics, and fishing

Surrounding Land Use: Forested 25%, beach 35%, urban-residential 2%, open area with grass and cement 38%

Sampling Site:  beach, banks altered, shoreline rip rap, bulkhead, collected wood/debris

Plants in area:

| Tidal Shallows Plants | water celery 15% | water chestnut 85% |
| --- | --- | --- |

Water depth: 1-5 ft. deep

Bottom Surface: rocky and muddy

| ITEM | Time | Reading 1 | Reading 2 | Comments |
| --- | --- | --- | --- | --- |
| Physical |  |  |  |  |
| Air Temperature | 10:20 AM | 19(C 62 (F |  |  |
|  | 11:20 AM | 21(C 68 (F |  |  |
|  | 1:20 PM | 21(C 70 (F |  |  |
| Wind Speed | 10:20 AM | 11-16 knots Beaufort | South |  |
|  | 11:20 AM | 10 knots |  |  |
| Cloud Cover | overcast |  |  | Water choppy |
| Weather today | Mostly cloudy and overcast BUT at 11:30 sun came out |
| Weather recently | Stormy and showers overnight, windy warm and sunny 2 days ago |
| Water Temperature | 10:15 AM | 62( F 18(C | 62( F 18(C |  |
|  | 10:45 AM | 61( F 17(C | 61( F 17(C |  |
|  | 11:15 AM | 62( F 18(C | 62( F 18(C |  |
|  | 12:10 PM | 63( F 19(C | 60( F 17(C | Second temp. in shady spot |
|  | 12:51 PM | 62( F 18(C | 62( F 18(C |  |
|  | 1:25 PM | 62( F 18(C | 62( F 18(C |  |
| Turbidity | 10:30 Am | 80 JTU | 80 JTU | Sight tube |
|  | 10:45 AM | 80 JTU | 80 JTU |  |
|  | 11:30 AM | 80 JTU | 80 JTU |  |
|  | 12:40 PM | 80 JTU | 80 JTU |  |
|  | 12:50 PM | 80 JTU | 80 JTU |  |
|  | 1:25 PM | 80 JTU | 80 JTU |  |
| Chlorophyll | 9:00 | 2.0 |  |  |
| Chemical |  |  |  |  |
| DO (drop kit) 9.0 mg/L each test | 10:15-1:25 PM | 9.0 mg/L | 17(C 63(F | 95% |
| pH – Indicator Sol. | 10:15-1:25 | 7.5 | 7.5 | 7.5 |
| pH pen | 10:15-1:25 | 8.0 | 8.1 | 7.9 |
| Phosphate |  |  |  |  |
| Nitrate |  |  |  |  |
| Alkalinity | 12:45 PM | 120 ppm |  |  |
| Salinity - %NaCl | 10:15-1:25 | .006 | .005 | .006 |
| Fish Catch | Number Caught | Species | CPUE | Seine – 1 pull 80 ft. |
|  | 4 | Blueback Herring |  |  |
|  | 1 | Pumpkinseed |  |  |
|  | 2 | Smallmouth bass |  |  |
|  | 1 | Spottail shiner |  |  |
|  | 6 | Striped bass |  |  |
|  | 5 | White perch |  |  |
|  | 1 | American Shad | Y-o-y (young of the year) |
| Tides | 10:08 AM |  |  |  |
|  | 10:35 AM |  | Falling |  |
|  | 10:40 AM |  | Falling |  |
|  | 11:28 AM |  | Rising |  |
|  | 12:05 PM |  | Rising |  |
|  | 12:40 PM |  | Rising |  |
|  | 1:05 PM |  | Rising |  |
|  | 1:45 PM |  | Rising |  |
| Currents | Wind was pushing stick upriver (north) – wind too strong to determine current I believe |
| Traffic | 12:45 PM | Very large Barge | South | loaded – possible fill or dirt |
| Other Items |  | Immature bald eagle |  |  |
|  |  | Gulls |  |  |
|  |  | cormorant |  |  |
|  | 2 | Monarch butterflies |  |  |