Snapshot Day 10/14/10

(Salt Front RM 36.0)

RIVER MILE 84.5

Mills-Norrie Point Environmental Center, Staatsburgh, NY, Dutchess County

Rebecca Houser, Dan Miller and SCA members

Bryan Woods, Poughkeepsie High School

33 – 10th graders

N41°51minutes    W73°54 minutes

Location: Sampling done Norrie Cove and the SW corner of Norrie Point Env. Center Patio.   East side of Hudson far from the main channel in a protected cove

Area: Substantial paved areas nearby, large environmental center building adjacent to the water.  Shallow cove, facing south onto the HR, nordered by RR embankment, parking lot & the environmental center.

Surrounding Land Use: 75% State Park; 15% Forested; 10% Beach

Sampling Site: Banks altered, Rip Rap

Shoreline: beach aarea, shore with bulkhead, shoreline rip rap, covered with vegetation (some duckweed on surface, water celery in the bay- mostly uprooted), banks altered for EEC building, riprap along RR tracks, collected wood and debris in shallow cove, piping entering river area

Plants in area: yes sampling site has plants

Water depth:  57-32 cm depth

River Bottom – weedy, muddy and rocky

| ITEM | Time | Reading 1 | Reading 2 | Comments |
| --- | --- | --- | --- | --- |
| Physical | Time |  |  |  |
| Air Temperature | 9.59 AM | 15(C 60 (F |  |  |
|  | 10:22 AM | 21(C 64 (F |  |  |
|  | 10:41 AM | 21(C 64 (F |  |  |
|  | 11:45 AM | 24(C 72(F |  |  |
|  | 12:49 PM | 21(C 64 (F |  |  |
| Wind Speed | Beaufort #1-2 | 1-3 knots | South |  |
| Cloud Cover | Partly cloudy |  |  |  |
| Weather today |  |
| Weather recently |  |
| Water calm | Water calm |
| Water Temperature | 10:45 AM | 13(C 56(F |  |  |
|  | 12:05 pm | 18 (C 64 (F |  |  |
| Turbidity Long Sight Tube | Time | cm |  |  |
| Sight tube | 1:00 PM | 10 cm | 8 cm | 9 cm average |
| Chlorophyll |  |  |  |  |
| Chemical |  |  |  |  |
| DO (drop count) | 10:50 AM | 9.0 mg/L 8 mg/L 8.5 average | 13(C | 78% |
|  | Noon | 8.0 mg/L 8.0 mg/L | 18(C | 83% |
| Salinity |  |  |  |  |
| - | 10:45 AM | 5 ppm (?) |  |  |
|  | 11:42 | 28 ppm |  |  |
| Fish |  |  |  |  |
|  | # of fish | size of largest | Fish Species |  |
|  | 24 |  | Pumpkinseed |
|  | 6 |  | Tessellated darter |
|  | 3 |  | American Eel |
|  | 12 |  | Spottail Shiner |
|  | 15 |  | Banded Killi |
|  | 1 |  | Black Crappie |
|  | 5 |  | American Shad |
|  | 5 |  | Blue Herring |
|  | 3 |  | Alewife |
|  | 2 |  | White Perch |
|  | 1 |  | Golden Shiner |
|  | 1 |  | Goldfish |
|  | 1 |  | Striped Bass |
|  | 1 |  | Brown Bullhead |
|  | 1 |  | Blue Claw Crab (Male) |
| Tides | time | cm | Time | cm |
|  | 9:55 AM | 21 cm | 10: 55 AM | 8 cm falling |
|  | 10:05 AM | 18 cm falling | 11:05 AM | 6 cm falling |
|  | 10:15 AM | 15.5 cm falling | 11:30 AM | 2 cm falling |
|  | 10:25 AM | 13.5 cm falling | 11:40 AM | 1.9 cm falling |
|  | 10:35 AM | 10 cm falling | 11:50 Am | 0.5 cm falling |
|  | 10:45 AM | 9 cm falling | 12:00 noon | 0 cm falling |
| Currents | 10:00 AM | Still | 1 m/15 sec |  |
|  | 10:45 AM | Ebb | 3m/57 sec |  |
|  | 11:50 AM | Still | 4.6 m/135 sec |  |