Day in the Life of the Hudson River 10/14/21

Sarah Lawrence College CURB: Beczak, Yonkers

RIVER MILE: 18

Salt Front: ~ 49

Eli Caref & Sarach Lawarence College Center for Urban River at Beczak

2 students & 3 adults

Latitude 40.938483 N & Longitude -73.90291 W

Location: Sarah Lawrence College CURB at Beczak, Habirshaw County Park, Yonkers, Westchester County, NY

Area: 2 acre riverfront county park covered mostly by a grass lawn leading down to the river where it meets a tidal wetland and sandy beach. Property used for fishing, boats, seining, field trips and some education programs.

Surrounding Land Use: 75% Urban/Residential; 25% Beach/Waterfront

Sampling Site: Sandy beach, tidal marsh area covered with vegetation, banks altered, large riprap on shoreline, collected wood/debris in area

Plants in area: No plants in the water area; however in the marsh, there is mud wort, reed grass, salter cordgrass, big cordgrass

River Bottom: Muddy

*NR = Not read/recorded

| ITEM | Time | Reading | Comments |
| --- | --- | --- | --- |
| Physical |
| Air Temperature | 10:33 AM | 21.1 o C | 70 o F |  |
| Wind Speed: | 10:33 AM | Anemometer NR | Beaufort 1 | Direction NW |
| Weather today | 10:33 AM | <25% cloud cover | No Rain |  |
| Weather the past 3 days: | NR |
| Tides- | Time | Rising, Falling, Unchanged | Height (cm) |  |
|  | 10:33 AM 11:22 AM | Falling Rising – see note! | 12 cm 12 cm | *LT was at 11:01 AM so sampled on either side of the falling and rising tide! |
| Current- | Time | Cm/sec | Knots | North/South | Ebb/Flood/Still |
|  | 10:40 AM | 15 | 0.29 | South | Ebb |
| Water Temperature- | 10:57 AM | 20.5o C | 68.9o F |  |
| Turbidity- YSI probe | 10:57 AM | 74.8 cm |  |
| Chemical |
| Salinity- Meter/probe | 10:57 AM | 6.65 ppt |  |  |
| Standardized Salinity – HR Quantab | 10:57 AM | 6,256 ppm (6.3 ppt) |  |  |
| DO – meter/prob | Time | Temp | ppm DO | % saturation |
|  | 10:57 AM | 20.5 o C | 6.72 | 70% |
| pH – meter | 10:57 AM | 7.51 |  |
| Nitrates- NR |  |  |  |
| Phosphates- NR |  |  |  |
| Biological |
| Fish – seine 11:05 AM | Number | Name | Length of longest | Length of smallest |
|  | 1 1 1 1 | Bay Anchovy Atlantic Silverside White Perch Striped Bass | 6.5 cm 1.7 cm 18 cm 19 cm |  |
| Fish Totals | TOTAL: 4 | Diversity: 4 |  |  |
| Macroinvertebrates | Number | Name | Length of longest | Length of smallest |
|  | 8 1 | Blue Crab Crangon Shrimp (Sand) | 8 cm 4 cm | NR |
| Macroinvertebrate Totals | TOTAL: 9 | Diversity: 2 |  |  |
| Sediment Core |
| Length | H2S smell | Oxid Top | Oil | Grain Size | Other Features |
| 24.13 cm | Yes (mild smell) | No | No | Abundant: clay, mud, sand Common: pebbles, leaves | Rare: wood |
| Boats-NR |
|  | Time | Name | Color | North/Southbound | Light/Loaded |
| Commercial |  |  |  |  |  |
| Residential |  |  |  |  |  |