Snapshot Day 10/7/08 Data

(Salt Front RM 63.4)

RIVER MILE 25W

Piermont Pier

Lamont-Doherty Earth Observatory

Ellen Pollina, Brian Newburger– Tappan Zee High School AP Bio. – 33 students

Tom Mullane & Sheryl Turk - Pearl River High School APES – 37 students

Jen Mazza – Clarkstown South High School - 6 HS students

Latitude N 41 degrees 02’591”    Longitude W 73 degrees 53’758"

Location: Piermont Pier, Piermont NY

Area: Man made fishing/shipping pier at the east end, long pier with paved roadway and vegetation along both sides

Surrounding Land Use:  Urban/residential 80% , Forested 20%

Sampling Site:  Pier, roadway in center of whole pier, parking area at end, Plants and trees along side.  Shoreline Rip Rap, collected wood in area and piping entering river on the South of sampling site

Plants in area: few plants in the water but lots of plants along pier

Water depth: Varied by location on the pier –

River Bottom – sandy/rocky bottom with marsh grass growing in or near the water

Plants in area: sumac 30%; marsh plants 70%; reeds & cattails

| ITEM | Time | Reading 1 |  | Comments |
| --- | --- | --- | --- | --- |
| Physical |  |  |  |  |
| Air Temperature | 9:33 AM | 12.5(C 54.5 (F |  |  |
|  | 10:00 AM | 15 (C | 14.7 (C |  |
|  | 10:20 AM | 13.6(C 55.4 (F | 13.6(C 57.4 (F |  |
|  | 10:53 AM | 15.1 (C 57.2 (F |  |  |
|  | 11:06 PM | 14.9 (C 58.5 (F |  |  |
|  | 11:19 AM | 17.7 (C 63 (F | 16.6 (C 62.1(F |  |
|  | 12:59 PM | 17.5 (C |  |  |
|  | 1:15 PM | 15.5 (C |  |  |
|  | 1:32 PM | 17.6(C 65.5 (F |  |  |
| Wind Speed | Time | Beaufort # | Anenometer | Direction |
|  | 9:30 AM | 1 | 2.5 knots | North |
|  | 10:20 AM | 0.0 | 0.6 knots 3.6 knots | NW ->SE |
|  | 10:53 AM |  | 3.6 knots 1.6 knots | NW anonometer |
|  | 11:19 AM | 1 | 1.8-2.0 knots 2.0 knots | North |
|  | 11:30 AM | 2-3 | 6.9-9.3 knots | North |
|  | 12:35 PM | 2-3 | 4.5–7.0 knots |  |
|  | 12:59 PM | 3 3 | 7.0 knots 8-12 knots |  |
|  | 1:15 PM | 2 | 4.8-5.6 |  |
|  | 1:32 PM | 3 | 6.8-7.9 |  |
| Cloud Cover | clear |  |  |  |
| Weather today | Clear and cool – wind started to pick up at about 10:30 AM |
| Weather recently | Mon – little rain, and it has been cooler than normal |
| Water Temperature | 10:15AM | 17(C |  | SURFACE SAMPLE |
|  | 10:34AM | 17(C |  |  |
|  | 11:45AM | 17(C |  |  |
|  | 12:50PM | 18(C |  |  |
|  | 1:20 PM | 19(C |  |  |
| Water Temperature |  |  |  | BOTTOM SAMPLE |
|  | 9:30AM | 18(C |  |  |
|  | 10:30AM | 16(C |  |  |
|  | 11:15AM | 18(C |  |  |
|  | 12:35PM | 19(C |  |  |
|  | 1:15PM | 19(C |  |  |
| Turbidity – All readings are an average of 2 or 3 readings taken in each of 2 groups for each time period | 9:30 AM | 40.7cm |  | Long site tube |
|  | 10:30AM | 37.5 |  |  |
|  | 10:55AM | 26.5 cm |  |  |
|  | 11:23AM | 20.05 cm |  |  |
|  | 11:40AM | 26.45 cm |  |  |
|  | 12:40PM | 35.5 cm |  |  |
|  | 1:00 PM | 30.5 cm |  |  |
|  | 1:20 PM | 29.0 cm |  |  |
| Turbidity | 9:30 AM |  |  | Small site tube |
|  | 10:30AM | 20 JTU |  |  |
|  | 10:55AM | 20 JTU |  |  |
|  | 11:23AM | 25 JTU |  |  |
|  | 11:40AM | 15 JTU |  |  |
|  | 12:40PM | 25 cm |  |  |
|  | 1:00 PM | 20 cm |  |  |
|  | 1:20 PM | 20 cm |  |  |
| Chlorophyll | 9:30 AM | 1.35 |  |  |
|  | 10:30AM | 0.3 |  |  |
|  | 10:55AM | 1.4 |  |  |
|  | 11:23AM | 2.0 |  |  |
|  | 11:40AM | 2.5 |  |  |
|  | 12:40PM | 0.8 |  |  |
|  | 1:00 PM | Not read |  |  |
|  | 1:20 PM | 1.75 |  |  |
| Chemical | SURFACE WATER SAMPLES |
| DO | 10:15AM | 8.0 mg/L | 17(C | 80% |
| Drop count | 10:34AM | Spilled – no reading | 17(C |  |
|  | 11:45AM | 13.0 mg/L | 17(C | Over 100% |
|  | 12:50PM | 9 mg/L | 18(C | 94% |
|  | 1:20 PM | 5 mg/L | 19(C | 55% |
| pH | 10:15AM | 7.4 |  |  |
| colorimeter | 10:34AM | 7.5 |  |  |
|  | 11:45AM | 7.5 |  |  |
|  | 12:50PM | 7.7 |  |  |
|  | 1:20 PM | 7.0 |  |  |
| Phosphate | 10:15AM | No results |  |  |
| colorimeter | 10:34AM | No results |  |  |
|  | 11:45AM | 4.96 mg/L | Seems too high? |  |
|  | 12:50PM | 5 mg/L | Seems too high? |  |
|  | 1:20 PM | .44 mg/L |  |  |
| Nitrate | 10:15AM | No results |  |  |
| Drop count | 10:34AM | 0.44 ppm |  |  |
|  | 11:45AM | 0.1 ppm |  |  |
|  | 12:50PM | 0.88 ppm |  |  |
|  | 1:20 PM | 0.88 ppm |  |  |
| Alkalinity | 10:15AM | 100 ppm |  |  |
| Drop count | 10:34AM | 80 ppm |  |  |
|  | 11:45AM | 56 ppm |  |  |
|  | 12:50PM | 60 ppm |  |  |
|  | 1:20 PM | 36 ppm |  |  |
| Salinity | 10:15AM | 8.0 ppt |  | Hydrometer |
|  | 10:34AM | 6.7 ppt |  |  |
|  | 11:45AM | 6.7 ppt |  |  |
|  | 12:50PM | 7.0 ppt |  |  |
|  | 1:20 PM | 7.2 ppt |  |  |
| Chemical | BOTTOM WATER SAMPLES |
| DO | 9:30AM | 8.0 mg/L | 18(C | 82% |
|  | 10:30AM | 5.0 mg/L | 16(C | 54% |
|  | 11:15AM | 8.0 mg/L | 18(C | 80% |
|  | 12:35PM | 5.0 mg/L | 19(C | 54% |
|  | 1:15PM | 9.0 mg/L | 19(C | 95% |
| pH | 9:30AM | 7.5 |  |  |
|  | 10:30AM | 7.5 |  |  |
|  | 11:15AM | 7.5 |  |  |
|  | 12:35PM | 7.5 |  |  |
|  | 1:15PM | 7.5 |  |  |
| Phosphate | 9:30AM | 0.10 mg/L |  |  |
|  | 10:30AM | 0.40 mg/L |  |  |
|  | 11:15AM | 0.08 mg/L |  |  |
|  | 12:35PM | 0.5 mg/L |  |  |
|  | 1:15PM | 0.6 mg/L |  |  |
| Nitrate | 9:30AM | 0.3 ppm |  |  |
|  | 10:30AM | 0.3 ppm |  |  |
|  | 11:15AM | 0.15 ppm |  |  |
|  | 12:35PM | 0.44 ppm |  |  |
|  | 1:15PM | 0.44 ppm |  |  |
| Alkalinity | 9:30AM | 120 ppm |  |  |
|  | 10:30AM | 35 ppm |  |  |
|  | 11:15AM | 38 ppm |  |  |
|  | 12:35PM | 80ppm |  |  |
|  | 1:15PM | 80 ppm |  |  |
| Salinity | 9:30AM | 7 ppt |  | refractometer |
|  | 10:30AM | 6 ppt |  |  |
|  | 11:15AM | 6 ppt |  |  |
|  | 12:35PM | 6 ppt |  |  |
|  | 1:15PM | 6 ppt |  |  |
| Tides | Time | Tide Stick |  |  |
|  | 9:33 AM | 25 cm |  |  |
| Setting a tide stick | 10:23AM | 25 cm | *falling | *the tide was dropping from 9:33 AM until 10:30 AM when it hit low tide |
|  | 10:48AM | 29.5 cm | rising |  |
|  | 11:13AM | 33 cm | rising |  |
|  | 11:35AM | 40 cm | rising |  |
|  | 12:34PM | 57 cm | rising |  |
|  | 12:56PM | 66 cm | rising |  |
|  | 1:23PM | 72 cm | rising |  |
| Measuring down with tape off side of wood piling pier | 9:33 AM | 55 cm | falling |  |
|  | 10:28AM | 53 cm cm | falling |  |
|  | 10:48AM | 57 cm | rising |  |
|  | 11:16AM | 63 cm | rising |  |
|  | 11:37AM | 80 cm | rising |  |
|  | 12:37PM | 84 cm | rising |  |
|  | 12:58PM | 107 cm | rising |  |
| Currents | Time | Cm/60 secs | Cm per sec | Knots/direction |
| *current differs from the main stem. AT 10:35 AM visually can see the switch in current from a line on the water in the main stem | 9:50AM | 90cm/60 secs. | 1.5 cm/sec | 0.3 knots N flood* |
|  | 10:02AM | 364cm /60 secs. | 6.0 cm/sec | 0.12 knots S ebb |
|  | 10:35AM | 1061cm /60 secs | 17.7 cm/sec | .35 knots |
|  | 11:00AM | 1840 cm/60 secs | 30.1 cm/sec | 0.61 knots |
|  | 11:26AM | 1400 cm/60 secs | 23.3 cm/sec | 0.476 knots ebb |
|  | 11:42AM | 1434 cm/60 secs | 23.9cm/sec | 0.478 knots S ebb |
| •expect error here? | •1:20 PM | 3286.8 cm/60secs | 54.78 cm/sec | 1.10 knots N flood |
|  | 12:45PM | 102cm/60sec | 1.6 cm/sec | .03 knots N flood |
|  | 1:05 PM | 860cm/sec | 14.33cm/sec | .29 knots Flood |
|  | 1:17 PM | 1460 cm/sec | 24.3 cm/sec | .49 knots Flood |
|  | 1:36 PM | 1400 cm/sec | 23.3 cm/sec | .46 knots Flood |
| Fish Catch | Number Caught | Species | Measure of largest | Seine 30 m |
| Northside of pier | 48 | Atlantic Silverside | 11.5 cm | 10:00 AM |
| 5 rotations – | 1 | Striped Bass | 5 cm |  |
| Each group 1 seine | 4 | Juvenile Blue Crabs | 2 cm |  |
| But with 2 nets | 2 | Blue Crab | 6 cm | Diversity 4 |
|  | 2 | Shore shrimp | 2 cm | 57 total |
|  | 17 | Atlantic Silverside | 12 cm | 10:40 AM |
|  | 2 | Naked Goby | 4 cm |  |
|  | 5 | Striped Bass | 1 cm | Diversity 4 |
|  | 20 | Blue Crab | 6 cm | 44 total |
|  | 7 | Atlantic Silverside | 11 cm | 11:45 AM |
|  | 2 | Striped Bass | 10.5 cm |  |
|  | 1 | Comb Jellies | 13 cm | Diversity 4 |
|  | 10 | Blue Crab | 9 cm | 20 total |
|  | 10 | Atlantic Silverside | 11 cm | 12:30 PM |
|  | 3 | Striped Bass | 9 cm |  |
|  | 3 | Naked Goby | 2 cm |  |
|  | 3 | Striped Bass | 9 cm |  |
|  | 9 | Blue Crab | 6 cm |  |
|  | 3 | Comb jellies | 2 cm | Diversity 6 |
|  | 2 | Shore shrimp | 2 cm | 33 total |
|  | 2 | Striped Bass | 10 cm | 1:15 PM |
|  | 2 | Blue Crab | 2 cm | Diversity 3 |
|  | 3 | Comb Jellies |  | 7 total |
|  |  | Grand Total |  | Diversity 6 |
|  |  |  |  | Count 161 |
| Cores | Length | Abundant | Common | Rare | Comments |
| 9:30 AM – water | 16 cm 6 cm top grainy (sand & Gravel) bottom smooth clay | Clay | Sand | Gravel, Pebbles | H2S smell |
| 10:06 AM – water 20 cm deep | 13 cm - 4 cm top mainly pebbles bottom 9 cm mainly clay | Clay, | Sand Pebbles | Mud Gravel | H2S smell 1 crab in top 4 cm Oxidized material in a pocket in the clay down by bottom |
| 10:20 AM – water 34 cm deep | 15 cm – top 12 cm watery & sandy, from12cm to 15 cm gravel | Sand – | Gravel Pebbles | Brick | H2S smell medium |
| 10:50 AM – water 35 cm | 16 cm – top 8 cm clay, 2 cm sand, 6 cm gravel | Sand | Clay Gravel | Pebbles | H2S smell |
| 11:20 AM – water 52 cm | 27 cm – top 14 cm gravel and sand | Mud | Clay, sand, gravel | Pebbles Leaves Wood Shells Brick | Dense feel – sandy clay, hard H2S smell |
| 11:50 PM – water 48 cm | 11 cm - top 5cm sand | Sand | Gravel Pebbles | Clay Shells Brick | Small bit of H2S odor |
| 12:30 PM – water 58 cm (Marsh core) | 13 cm top 8 cm lots of fibers, at 2 cm a leaf | Sand Living Vegetation | Leaves | Clay Gravel Pebbles Macroinvert | Small bit of H2S odor Lightly oxidized top |
| 1:00 PM – water 60 cm | 13 cm mud top 1cm, rhizomes between cm 4 and cm 9 | Sand | Rhizome & Living Vegetation | Clay Mud Gravel Pebbles | Small bit of H2S odor |
| 1:20 PM – water 32 cm (core near bank) | 6 cm core | Clay | Pebbles | Mud Gravel Plant material | Rock in top corner, clay and rhizomes at bottom H2S odor |