Snapshot Day 10/8/09 Data

(Salt Front RM 60.3)

RIVER MILE 84.5

Mills-Norrie Point Environmental Center, Staatsburgh, NY, Dutchess County

Jean Villa McAvoy & Laurie Fila, Hudson River National Estuarine Research Reserve (HRNERR)

Barbara Procario, VanWyck Junior High School, Wappingers School District

83 Seventh Graders

N41°51minutes    W73°54 minutes

Location: Sampling done Norrie Cove and the SW corner of Norrie Point Env. Center Patio.   East side of Hudson far from the main channel in a protected cove

Area: Substantial paved areas nearby, large environmental center building adjacent to the water.  Shallow cove, facing south onto the HR, nordered by RR embankment, parking lot & the environmental center.

Surrounding Land Use: 75% State Park; 15% Forested; 10% Beach

Sampling Site: Banks altered, Rip Rap

Shoreline: beach aarea, shore with bulkhead, shoreline rip rap, covered with vegetation (some duckweed on surface, water celery in the bay- mostly uprooted), banks altered for EEC building, riprap along RR tracks, collected wood and debris in shallow cove, piping entering river area

Plants in area: 2% of water in sampling site is covered with plants.

Trapa Natans – 15%

Duckweed – 15%

Spiney Naiad - ~5%

Eurasian Water Milfoil - 12%

Phragmites – fringe along head of cover

Narrow leaved cattail

Water depth:  57-32 cm depth

River Bottom – weedy, muddy and rocky

| ITEM | Time | Reading 1 | Reading 2 | Comments |
| --- | --- | --- | --- | --- |
| Physical | Time |  |  |  |
| Air Temperature | 10:00 am | 15(C |  |  |
|  | 10:40 am | 16(C |  |  |
|  | 12:00 PM | 15(C |  |  |
|  | 12:40 PM | 19(C |  |  |
| Wind Speed | Beaufort #1 | 1-3 knots |  |  |
| Cloud Cover | cloudy |  |  |  |
| Weather today | Cloudy but no rain |
| Weather recently | warm and mild |
| Water calm | Water calm |
| Water Temperature | 9:54 am | 16(C 18(C | 17(C |  |
|  | 10:36 am | 16(C 17(C | 16.5(C |  |
|  | 11:55 am | 17(C 19.5(C | 18.25 (C |  |
|  | 12:30 pm | 20 (C 18 (C | 19 (C |  |
| Turbidity Long Sight Tube | Time | cm |  |  |
| Sight tube | 10:06 AM | 17 cm |  |  |
|  | 10:45 AM | 11 cm |  |  |
|  | 12:40 PM | 14 cm |  |  |
| Chlorophyll | 12:15 PM | 0.5 |  |  |
| Chemical |  |  |  |  |
| DO (drop count) | 9:56 AM | 3.0 mg/L | 16(C | 30% |
| Samples taken in direct sum | 10:45 am | 8.0 mg/L | 17(C | 85% |
|  | 10:50 pm | 11.mg/L | 17(C | 115% |
|  | 12:50 pm | 10. mg/L | 20(C | 95% |
|  | 12:09 pm | 9 mg/L | 19.5(C | 96% |
| pH | 9:95 am | 7.0 |  |  |
|  | 10:45 am | 8.0 |  |  |
|  | 12:05 pm | 8.0 |  |  |
|  | 12:45 pm | 8.0 |  |  |
| Salinity | 9:53 am | 0.1ppt |  |  |
| -drop count kit |  |  |  |  |
| Fish |  |  | 4 seines |
|  | # of fish | size of largest | Fish Species |
|  | 58 | 9.75 cm. | Banded killifish |
|  | 21 | 12 cm. | Pumpkinseed sunfish |
|  | 9 | 11 cm. | Shiners (unidentified) |
|  | 8 | 5.5 | Sunfish (unidentified) |
|  | 8 | 11.5 cm. | Spottail shiner |
|  | 5 | 9cm. | Tessellated darter |
|  | 4 | 11.5 cm. | Large mouth bass |
|  | 1 | 8.5cm. | Brown bullhead |
|  | 1 | 8 cm. | Golden shiner |
|  |  |  | Total # fish species: 9 |
|  |  |  | Total # fish: 115 |
|  | # macros | size of largest | Macroinvertebrate Species |
|  | 35 | 4.5 cm. | Blue crab |
|  | 1 |  | Spiny-cheek crayfish |
|  |  |  | Total # macroinvertebrate species: 2 |
|  |  |  | Total # macroinvertebrates: 36 |
| Tides | time | cm | Rising/falling |
|  | 8:30 PM | 10 cm |  |  |
|  | 10:09 PM | 6 cm | falling |  |
|  | 10:21 PM | 6 cm | unchanging |  |
|  | 10:30 PM | 7 cm | rising |  |
| Currents | 9:54 PM | Ebb | 7-10 cm/sec |  |
|  | 10:09 PM | Ebb | 7-10 cm/sec |  |
|  | 10:50 PM | Flood |  |  |
|  | 12:04 PM | Flood |  |  |
|  | 12:45 PM | Flood |  |  |
| Core sample #1 – noon | Length 14 cm | Common – Soft and gritty, it did smell like sulfur, color dark grey | Rare |  |
| Traffic | 11AM | Sailboat | White | south |
|  | 11:15 AM | Sailboat | White/Blue | South |
|  | 12:06 PM | Motorboat | White | South |
|  | 12:30 PM | Barge |  | South |
| Other Items | 9:35 am | Bald Eagle |  |  |