Snapshot Day 10/14/10

(Salt Front RM 36.0

RIVER MILE 58

Kowawese Unique Area, Plum Point, New Windsor, Orange County, NY

Judy Onufer & Pam Golben Museum of the Hudson Highlands

Dr. Bhalla and Mt. St. Mary’s College Students

Bernadette Kleister, Bishop Dunn Memorial School  - 7th grade – 35 students

GPS Latitude 41(27’44”N Longitude 74(00’41”W

| The waterfront at Kowawese | The female blue crab (5 inch carapace) |
| --- | --- |

Location: Sandy beach at Kowawese, New Windsor, Orange County, Public Shore, Picnic Area

Area: Sandy beach with scattered tidal debris, forested above beach to South, grass and trees and picnic area to North.  Rip Rap, broken wood in boat launch area. Parking above beach area.  No swimming.  People fish and launch boats here.

Surrounding Land Use: Forested 25%, beach 50%, Urban/residential 25%

Sampling Site:  sandy beach (cove), rip rap in area of sampling site, Much wood washed up on beach.

Plants in area: < 50%of sampling area – 75% of plants Water celery – sporadic not dense; 25% - other vegetation.

Other trees in area – mostly wooded – oak, tulip, poplar and maple.

Water depth:  <1 meter; Ebb tide

River Bottom –Mostly mud/sand with a few larger rocks.

| ITEM | Time | Reading 1 | Reading 2 | Comments |
| --- | --- | --- | --- | --- |
| Physical |  |  |  |  |
| Air Temperature | 10:30 AM | 11(C 52(F |  |  |
| Wind Speed | 0 - calm |  |  |  |
| Cloud Cover | Partly cloudy |  | Weather became overcast by 12:30 PM |
| Weather today | Sunny 60s |
| Weather recently | rained previous day |
| Water Surface | calm |
| Water Temperature | 9:30 AM | 59.9 ( F 15.5 (C |  |  |
|  | 10:10 AM | 60.3( F 15.7(C |  |  |
|  | 11:45 AM | 64.6( F 18.1(C |  |  |
|  | 12:25 PM | 65.3( F 18.5(C |  |  |
| Water Calm | yes |  |  |  |
| Turbidity Short sight tube | 9:30 AM | 20 JTU 40 50 40 |  | 37.5 JTU avg. |
| Chlorophyll | 9:15 AM | 0.1 |  |  |
| Chemical |  |  |  |  |
| DO (drop kit) | TIME | Temp | DO | % Sat |
| DO trended upward over the study period. | 9:30 AM | 15.5 (C | 7 | 69 |
|  | 10:10 AM | 15.7 | 8 | 80 |
|  | 11:45 AM | 18.1 | 9 | 93 |
|  | 12:25 PM | 18.5 | 9.3 | 98 |
| pH - meter | 9:30 AM | 6.8 6.7 7.0 6.0 |  | 6.6 average |
| Salinity - meter | TIME | Conductivity/ mS/cm | ppm Cl- | ppm Total Salinity |
| Fluctuated over the study period although highest salinity was measured at the time of low tide counter to what would be anticipated if salt values were due to tidal action | 9:30 AM | 250 | 29 ppm | 52 ppm |
|  | 10:10 AM | 272 | 38 ppm | 69 ppm |
|  | 11:45 AM | 300 | 68 ppm | 123 ppm |
|  | 12:25 PM | 272 | 38 ppm | 69 ppm |
| Fish Catch 35 ‘ X 3 ‘ with ¼ inch mesh | Time | Species | # | Size of largest (inches) |
|  | 9:30 AM X 2 pulls | White Perch | 1 | 3 |
|  |  | Tesselated Darter | 1 | 2.5 |
|  |  | Herring | 20 | 2.5 |
|  |  | Blue Crab - F | 1 | 5 |
|  |  | Blue Crab – M | 1 | 0.5 |
|  | 10:15 AM X 3 pulls | Eel | 1 | 4 |
|  |  | Striped Bass | 4 | 2 |
|  |  | Banded Killifish | 1 | 1 |
|  |  | Spottail Shiner | 1 | 2.5 |
|  |  | White Perch | 5 | 5 |
|  |  | Tesselated Darter | 1 | 2.5 |
|  |  | Herring | 14 | 2 |
|  |  | Blue Crab - F | 3 | 5 |
|  |  | Blue Crab – M | 2 | 0.5 |
|  | 11:45 AM 1 pull | Striped Bass | 2 | 2 |
|  |  | Spottail Shiner | 4 | 2 |
|  |  | Herring | 20 | 2.5 |
|  |  | Gizzard Shad | 1 | 6 |
|  | 12:30 PM – 2 pulls | Killifish | 1 | 3 |
|  |  | Spottail Shiner | 3 | 2.5 |
|  |  | Herring | 27 | 2.7 |
| Tides | Time | Height in cm | Rate of change | Rising/falling |
|  | 8:32 AM | 33 cm |  |  |
|  | 9:13 AM | 25 cm |  | Falling |
|  | 9:35 AM | 20 cm |  | Falling |
|  | 10:07 AM | 15 cm |  | Falling |
|  | 11:38 AM | 11 cm |  | Falling |
| Currents | Very little | Water very quiet and still |  |  |
| Core | 5 cm | 3 cm top – sandy/pebbly | 2 cm lower - clay-like – sulfur odor |  |
| Traffic |  |  |  |  |
| Other | We had an outstanding day! In addition to the experience of collecting research data at Kowawese Unique Area, Mrs. Kleister’s 7th grade science class had the added bonus of working with Dr. Bhalla and her students from Mt. St. Mary College. They used Vernier probes to check measurements of pH, conductivity for salinity assessment and temperature. We were also visited by staff members from the DEC who arrived by boat with tagged blue crabs being readied for release. |