Snapshot Day 10/14/10 Data

(Salt Front RM 36)

RIVER MILE 76

Waryas Park, Poughkeepsie, Dutchess County

Nina, Clearwater

Jacob Lawrence, Arlington High School,  11-12th grade, 5 students

N 41 – W 73

Location: Waryas Park, Poughkeepsie, New York.

Area: public park, pier, grassy, parking lot.  Park used for fishing, small boat launch, another pier for small boat launching

Surrounding Land Use: 50 % urban/residential; 35% Industrial/commercial; 15% forested

Sampling Site: shoreline is riprap, vegetation, banks altered

Plants in area: ~ 25% urban/residential, 50% forested, 25% industrial/commercial.

Tidal Shallows: Water celery 80%, Water Milfoil 10%

Water depth:  67 cm.

River Bottom –muddy, rocky

| ITEM | Time | Reading 1 | Reading 2 | Comments |
| --- | --- | --- | --- | --- |
| Physical |  |  |  |  |
| Air Temperature | 12:50 PM | 18.4(C |  |  |
| Wind Speed |  | South |  |
| Cloud Cover | Partly cloudy to mostly cloudy | No rain |  |  |
| Water | Calm |
| Weather recently | mid 60s , rain on and off |
| Water Temperature | 1:05 PM | 15.1(C 15.2 15.2 | 59.2 (F 59.3 59.36 | Surface temp. |
|  | 1:05 PM | 15.1(C 15.1 15.2 | 59.2 (F 59.3 | 1 meter |
|  | 1:05 PM | 15.2(C | 59.3 (F | 2 meter |
| Turbidity | 11:15 AM | 43 cm 43 cm |  |  |
| Chlorophyll | 11:24 AM | 1.0 |  |  |
| Chemical |  |  |  |  |
| DO (Test tabs) | 10:30 AM | 15.1(C | 9.0 ppm | 87% |
|  | 11:30 AM | 16.1(C | 7 ppm | 70% |
| pH – indicator solution | Time | Colorimeter | Meter |  |
|  | 11:10 AM | 7.5 7.5 | 7.36 7.4 |  |
|  | 12:55 AM | 7.5 7.5 | 7.5 7.26 |  |
| Salinity - Quantab testtabs- low chloride | 11:30 Am | Scale of strip is 1.0 = 28 ppm | Strip reads 0.8, 0.8, 0.8 results <28 ppm chloride | <35 ppm salinity |
| Conductivity | 11:30 AM | Millisiemens 185.9 186.2 181.9 234.5 |  |  |
| Fish Catch | Number Caught | Species | Largest |  |
| Noon | 3 | Spottail Shiner |  | Total 4 Species 2 |
|  | 1 | Pumpkin Seed Sunfish |  |  |
| 12:45 PM | 5 | Spottail Shiner |  | Total 10 Species 4 |
|  | 3 | Pumpkin Seed Sunfish |  |  |
|  | 1 | Juvenile Striped Bass |  |  |
|  | 1 | Bullhead Catfish |  |  |
| Tides | 10:26 AM | 67 cm |  |  |
|  | 11:10 AM | 66 cm | Falling |  |
|  | 12:26 AM | 57 cm | Falling |  |
| Currents | 10:30 AM | 1980 cm/60 secs | 33 cm/sec | ebb |
|  | 11:10 AM | 1424 cm/60 secs | 23.73 cm/sec | ebb |
|  | 12:20 PM | 1170 cm/60 secs | 19.5 cm/sec | ebb |
|  | 12:45 PM | 15 cm/60 secs | 0.25 cm/sec | Almost Still! |
| Core | Length of Core | Rare | Common | Abundant |
|  | 2.5 inches | Clay Sand Oyster Shells | Mud | Gravel Pebbles |