Snapshot Day 10/14/10 Data

(Salt Front RM 36)

RIVER MILE 96.5

Ulster Landing State Park, Town of Ulster, Ulster Co.

Latitude 42(N, Longitude 73(56’W

Lia Harris, Cary Institute of Ecosystem Studies

Dixon Onderdonk, Kingston High School 11/12th graders – 13 students

Location: Swimming beach, Ulster Landing Park, Town of Ulster, Ulster County

Area: fishing, swimming beach, has a building with restrooms

Surrounding Land Use: Beach 50%; Forested area 50%

Sampling Site: beach, altered bank with concrete bulkhead, wood debris driftwood, drainage from bulkhead north of site immediately, flotsam and jetsam in the water

Plants in area: yes

Water depth: 3- 4 ft.

River Bottom : sandy, and little muddy bottom

Plants: few plants - duckweed

| ITEM | Time | Reading 1 | Reading 2 | Comments |
| --- | --- | --- | --- | --- |
| Physical |  |  |  |  |
| Air Temperature | 10:35 AM | 17(C 64 (F |  |  |
| Wind Speed | 1 Beaufort | 1-3 kts. | 1-3 mph |
| Cloud Cover | partly cloudy | No rain |  |  |
| Weather today | Clearing in morning but clouding up around 1PM |
| Weather recently | last 2 days clear, heavy rain 3 nights prior |
| Water Temperature | 9:10 AM | 11.6(C 12.3 | 53.2(F 54 | 11.9(C 53.5(F |
|  | 10:32 AM | 15.6(C 15.6 | 60(F 60 | 15.6(C 60(F |
|  | 12:45 PM | 21.1(C 21.1 | 70(F 70 | 21.1(C 70(F |
| Water Surface | Choppy due to wind |  |  |  |
| Turbidity turbidimeter | 10:27 AM | 24.9 NTU 24.0 23.3 |  | 24.1 NTU |
| Chlorophyll | 12:06 PM | 1.0 |  |  |
| Chemical |  |  |  |  |
| DO – 3 readings *(Hach 840 colorimeter 16.5ppm); chemet 11ppm and 9 ppm | 10:30 AM | 12.2 mg/L *(average of 3 tests) | 11.9(C | 110% saturated |
| (Hach DR-890) | 10:09 AM | 9 mg/L | 16(C |  |
| pH | 10:08 AM | 7.3 7.0 | 7.15 average | Indicator sol. |
|  | 10:08 AM | 6.77 |  | meter |
| Phosphate | 10:55AM | 2.75 ppm 2.27 ppm |  | 2.46 ppm average |
| Nitrate - | 10:20 AM | 3.8 ppm 3.2 3.5 |  | 3.75 ppm (fairly high reading) |
| Alkalinity | 9:18 AM | 80 mg/L 80 mg/L |  | 80 mg/L |
| Salinity – titration | 10:34 AM | 80ppm |  |  |
| Quantabs | 10:34 AM | 28 ppm 28 ppm 45-3?? ppm | 28 ppm Cl | 35 ppm salinity |
| Fish Catch 27.5’seine X 3.5 X/1/8 inch mesh | Number Caught per seine | Species – 8 total | Length of largest |
|  | #1 | #2 | #3 | #4 | #5 |  |  |
| 11:15-1:15 PM- 5 seines |  |  | 4 |  |  | Pumpkinseed | 12 cm (total 4) |
| Pull 50 ft. | 30 | 20 | 11 | 16 | 2 | Spottail Shiner | 13 cm (total 79) |
|  |  |  |  |  | 2 | Bluegill | (total 2) |
|  | 1 |  | 1 |  |  | Banded Killifish | 5 cm (total 2) |
|  | 23 | 21 | 1 | 3 | 1 | White Perch | 13 cm (total 49) |
|  |  | 1 |  |  |  | Golden Shiner | 12 cm (Total 1) |
|  |  | 1 |  |  |  | Striped Bass | 11.5 cm (total 1) |
|  |  | 1 |  |  |  | Tessellated Darter | 5 cm (total 1) |
|  |  |  |  |  | 1 | Largemouth Bass | 40 cm (total 1) |
|  | 1 |  | 4 |  | 4 | Scud | (total 9) |
|  | 4 |  |  |  | 5 | Blue Crab | (total 9) |
| TOTALS | 34 | 44 | 17 | 19 | 6 |  |  |
| CPUE | 0.16 | 0.2 | 0.08 | 0.09 | 0.2 |  |  |
| Pull | Time | Catch | CPUE | PULL |
| Tides | 9:14 AM | Set stick |  |  |
|  | 9:44 AM | Falling | 74 cm away from stick | 2.1 cm/min |
|  | 10:15 AM | Falling | 1.2 m | 9.3 cm/min |
|  | 10:44 Am | Falling | 2.1 m | 3.3 cm/min |
|  | 11:14 AM | Falling | 3.1 m | 3.4 cm/min |
| Currents 9:25 AM | 393 cm/60 secs | 6.5 cm/sec. | 0.12 knots | North Ebb but windy |
| 9:40 AM | 393 cm/60 secs | 6.5 cm/sec | 0.12 knots | North Ebb but windy |
| Traffic | 9:45 AM | Sailboat |  | South |
|  | 9:58 AM | Cruise ship |  | South |
|  | 11:20 AM | Barge/tug | empty | North |
| Other Items | Kayak, speedboats and small sailboats |  |  |  |
| Core | Length | Top | Bottom |  |
|  | 16.3 cm | 6.3 cm top | 10 cm bottom | Mostly sand and clay with brick fragment in upper core |