Snapshot Day 10/18/11 Data

(Salt Front RM 35.7)

RIVER MILE 28

Nyack Memorial Park

Tom Perry - Nyack High School APES Class 50 students, 11-12th graders

Latitude 40(05.243’N, Longitude 73(54.988 ‘W

Location: Nyack Park where Nyack Brook feeds in

Area: Open and grassy, has a parking lot, used for picnics, fishing

Surrounding Land Use:  100% park

Sampling Site: beach, banks altered, riprap on shoreline, bulkhead

Plants in area: no water plants in area

Water depth: varied

River Bottom – sandy/muddy bottom , water calm

| ITEM | Time | Reading 1 | Reading 2 | Comments |
| --- | --- | --- | --- | --- |
| Physical |  |  |  |  |
| Air Temperature |  |  |  |  |
| Wind Speed |  |  |  |  |
| Cloud Cover | Clear |  |
| Weather today |  |
| Weather recently | Clear & warm |
| Turbididty | Lower tide | 41.5 Pier 46.0 Dock | Higher Tide | 55.0 Pier 60.0 Dock |
| Phosphate |  |  |  |  |
| Nitrate |  |  |  |  |
| Fish Catch Seine 12X4 | Number Caught | Species | CPUE | Seine |
|  | 22 | Atlantic Silversides | Menidia menidia |  |
|  | 6 (small) | Striped Bass | Morone Saxatilis |  |
|  | 7 | Mummichog | Fundulus Heteroclitus |  |
|  | 2 (large) | White Perch | Monroe Americana |  |
| Sediment Cores Station #10 Sandy Beach |  | Sandy, Pebbly Sediment |  |  |
| Tide | 10:00 | 1:00PM | 66 cm rise/3 hrs. |  |

Sketch Map of Sampling Site

Hudson River

Time:  _______10:00 am___   Tide:  ________Low_______

| Station # | Distance (m) | Salinity (ppt) | Temperature (ºC) | DO mg/L | pH |
| --- | --- | --- | --- | --- | --- |
| 1 | 0 | 0.2 | 15.7 | 8.02 | 8.07 |
| 2 | 20 | 0.0 | 15.5 | 7.9 | 8.06 |
| 3 | 30 | 0.5 | 15.0 | 7.43 | 8.0 |
| 4 | 40 | 0.5 | 15.1 | 7.56 | 7.9 |
| 5 | 50 | 0.2 | 15.1 | 7.05 | 7.84 |
| 6 | 60 | 0.4 | 15.2 | 7.47 | 7.91 |
| 7 | 70 | 0.4 | 15.4 | 7.65 | 7.85 |
| 8 | 80 | 0.4 | 15.6 | 6.8 | 7.75 |
| 9 | 90 | 1.6 | 15.5 | 7.4 | 7.99 |
| 10 | 100 | 0.5 | 15.4 | 7.7 | 7.96 |
| 11 | 120 | 0.6 | 15.4 | 8.2 | 7.91 |
| 12 | 140 | 0.9 | 15.8 | 7.3 | 7.96 |

NOTE:  Notice how conductivity was much higher at 1:15pm starting at station 6.  This represents the saltier water of the rising tide.  At stations 6,7 and 8, the bottom water is warmer than the surface water.  Why doesn’t the warm water rise to the top?  At 9,10 and 11, wave action has mixed the water more.

Data Table 2:  Time ______12:50 PM    Tide _____Higher______

| Station # | Distance (m) | Salinity (ppt) | Temperature (ºC) | DO mg/L | pH |
| --- | --- | --- | --- | --- | --- |
| 1 | 0 | 0.3 | 16.0 | 7.75 | 8.1 |
| 2 | 20 | 0.5 | 15.8 | 7.85 | 8.2 |
| 3 | 30 | 0.4 | 15.8 | 7.60 | 8.2 |
| 4 | 40 | 0.5 | 15.9 | 7.79 | 8.2 |
| 5 | 50 | 0.6 | 16.5 | 7.78 | 8.1 |
| 6 | 60 | 0.7 | 16.7 | 7.63 | 8.1 |
| 7 | 70 | 0.8 | 16.8 | 7.20 | 8.1 |
| 8 | 80 | 0.8 | 17.6 | 7.1 | 8.1 |
| 9 | 90 | 1.0 | 17.9 | 6.7 | 8.1 |

# Text boxes

1

2

3

4

Nyack Brook

5

6

7

8

9

10

11