Day in the Life of the Hudson River 10/16/18 Data

STONY POINT MARINA, STONY POINT

Rockland County, NY

RIVER MILE: 39

Salt Front: ~RM 24

North Rockland High School-

50 students 11th and 12th grade, 4 adults

Jeanne Maguire, North Rockland HS

Latitude 41.2245828 N & Longitude - 73.99639967 W

Location: Stony Point Marina Riverfront Park, City of Stony Point in Rockland County

Area: Located along the side of the road at the south end of the marina- forested in the wider area, pier, grassy, parking lot

Surrounding Land Use: 50% Industrial/Commercial; 35% Urban/Residential; 15% Beach

Sampling Site: Along the seawall, sandy beach, banks altered, riprap (large rocks)

Shoreline: Sandy, rocky with bits of brick, coal and slag

Water Depth: 3 feet

Plants in area: 2% seaweed; water chestnuts on shore

River Bottom description: rocky, sandy

| ITEM | Time | Reading | Comments |
| --- | --- | --- | --- |
| Physical |  |  |  |
| Air Temperature | 8:30 AM 9:10 AM 9:30 AM | 6.1 oC 9.4 o C 10 o C | 43 o F 49 o F 50 o F |  |
| Wind Speed: anemometer (a) | 8:55 AM 10:27 AM | 5.6 mph 14.6 mph | Beaufort 2 Beaufort 3 | Northwest Water is choppy |
| Weather today | No rain, partly cloudy(26-50%) |
| Weather recently | Rained on 10/15/18 less than an inch |
| Water Temperature | 8:56 AM 10:23 AM | 16 o C 18.8 o C | 60.8 o F 65.84 o F |  |
| Turbidity - long sight tube secchi disk | 11:10 AM | 20 cm 20 cm | *Data sheet doesn’t really specify what equipment they used |
| Chemical |  |  |  |
| Salinity- High Range Quantabs | 9:30 AM | Below Detection with this method |  |  |
| DO – drop count kit | Time | Temp | ppm DO | % saturation |
|  | 8:56 AM 10:23 AM | 18.8 o C 16 o C | *23 *25 | * D.O. Discount as not realistic -expect didn’t swirl as they titrated |
| pH – color match kit | 9:12 AM 9:32 AM 10:30 AM | 8 7.7 8 |  |
| Fish | Number | Name | Length of longest (in) |  |
| 10:45 AM Seine- 9 foot net | 10 23 | Herring (young) Striped Bass | 3 2-3 |  |
| Fish Totals | TOTAL: 33 | Diversity: 2 |  |  |
| Tides- Dock to water | Time | Rising, Falling, Unchanged | Height (cm) | Rate of Tidal Change (cm/min) |
|  | 9:15 AM 9:45 AM | - Falling | 55 56 | .033 |
| Current- | cm/second | Knots | North/South | Ebb/Flood/Still |
| *current pushed the orange to shore | 5.08 7.68 6.73 | 0.099 0.149 0.131 | South South South | Ebb Ebb Ebb |
| Core | Description | Rare | Common | Abundant |
|  | 7.62 cm | Clay Mud Shell bits Slag | Gravel Pebbles Brick | Sand |
| Boat Traffic – commercial | Name | Color | North or South | Loaded or Light |
| 11:46 AM |  | Red and Black | North | Light |
| Boat Traffic – recreational | Name | Color | North or South | Loaded or Light |
| 8:30 AM 11:00 AM | Sailboat – named ‘Sea…2’ | White | North | *anchored and left heading north |
| Other Observations | Bits of brick, lumps of coal, shell pieces on shoreline | 1 seagull 3 Canadian Geese | Water chestnut seeds |  |