Day in the Life of the Hudson River 10/13/22

Matthiessen Park, Irvington, NY

RIVER MILE: 25

Salt Front: ~ 76

Irvington UFSD- Amy Panitz

255 students & 32 adults

Latitude 41.04164 °N & Longitude –73.87398 °W

Location: Matthiessen Park, Irvington, NY

Area: The sampling beach has a pier, grassy area, large parking lot to the south. Area is primarily used for boating, jogging, walking, picnicking, and fishing

Surrounding Land Use: 30% Forested, 10% Beach, 60% Grass with playground

Sampling Site: Pier, forested, grassy, parking lot, beach, banks altered, riprap, wood bulkhead, pipe entering the water

Shoreline: 90% sandy and 10% rocky.

Water: 180cm depth, calm by the beach

Plants in area: few plants in the water

River Bottom: sandy and rocky

*NR = Not read/recorded

| ITEM | Time | Reading | Comments |
| --- | --- | --- | --- |
| Physical |
| Air Temperature | 11:25 AM | 20.6° C | 69°F |  |
| Wind Speed: | 11:30 AM | Anemometer 12 mph | Beaufort 2.5 | Direction S/SE |
| Weather today | 11:00 AM | > 75% cloud cover | Light rain on/off in the morning |  |
| Weather the past 3 days: | Sunny, high temps in low 70s, very little wind, no rain |
| Tides- | Time | Rising, Falling, Unchanged | Water Height (cm) |  |
|  | 9:45 AM- 11:45 AM | Rising | 33 cm 80 cm |  |
| Current- | Time | Cm/sec | Knots | North/South | Ebb/Flood/Still |
|  | 9:45 AM 11:00 AM 11:40 AM | 22 33.3 40 | NR | NR | Flood Flood Flood |
| Water Temperature- | 11:00 AM | 18°C | 64°F |  |
| Turbidity- Short Sight Tube (60 cm) | 11:10 AM | 46 cm |  |
| Chemical |
| Salinity- Hydrometer | 10:55 AM | 12 ppt |  |  |
| Standardized Salinity – Refractometer | 11:30 AM | 10,000 ppm |  |  |
| DO – Chemets Kit | Time 11:05 AM | Temp 18°C | ppm DO 9 ppm | % saturation NR |
| pH – Color Match Kit | 11:05 AM | 6 |  |
| Nitrates- NR |  |  |  |
| Phosphates- NR |  |  |  |
| Alkalinity- NR |  |  |  |
| Biological |
| Fish – Seine | Number | Name | Length of longest | Length of smallest |
| 9:45 AM- 11:30 AM | 7 3 1 | Atlantic Silverside Striped Bass Summer Flounder | 7 cm 10 cm 11 cm | 3 cm 9 cm |
| Fish Totals | TOTAL: 11 | Diversity: 3 |  |  |
| Macroinvertebrates | Number | Name | Length of longest | Length of smallest |
|  | 12 1 1 | Blue Crab Moon Jelly Oyster (alive) | 8 cm | 1 cm |
| Macroinvertebrate Totals | TOTAL: 13 | Diversity: 2 |  |  |
| Sediment Core - |
| Length | H2S smell | Oxid Top | Oil | Grain Size | Other Features |
| 11 cm | No | No | No | Abundant: sand Common: mud, pebbles | Rare: shells |
| Boats-NR |
|  | Time | Name | Color | North/Southbound | Light/Loaded |